## Slide 1: Evolutionary Computation for Speech Enhancement
By: Vince Fasburg and Josh Thomas

## Slide 2: Overview
Introduction
Background
  Weiner Filter
  Spectral Subtraction
  Noise Gate
Evolutionary Strategy
Results
Conclusions

## Slide 3: Introduction
Problem
Recover clean speech signal from audio corrupted by noise, such as road noise.
Approach
Combine several existing de-noising algorithms, using evolutionary strategies to tune parameters to recreate clean signal.

## Slide 4: Background: CMA-ES
Real-valued parameters make up individuals
Random mutation from mean every gen
Mutation in direction of eigenvectors of covariance matrix
Notes: Covariance matrix “learns” relationships between the variables.
Helps point mutation in the right n-dimensional direction, using these relationships.

## Slide 5: Background: Spectral Subtraction
Basic Algorithm:
Subtract power spectrum of noise only from that of noisy signal X2 = (Y2 – N2)1/2
Improvements:
Y values smoothed
Speech/Noise decision with hold times
Parameters: Noise Margin, Hang Over, Noise Smoothing Factor
Notes: Version we’re using:
S.F. Boll (1979): "Suppression of acoustic noise in speech using spectral subtraction."IEEE Transactions on ASSP 27: 113–120
Needs piece of signal that is noise only
Noise Margin = threshold of difference between Y and N that will be considered noise
Hang Over = number of samples that will be considered noise once noise flag is set

## Slide 6: Background: Wiener Filter
Estimate SNR = S2/N, similarly to Spectral Sub
Use SNR to find best gains for FIR filter
Apply filter to eliminate noise
Parameters: SNR Smoothing Factor
Notes: Our Code adapted from Two-Step Noise Reduction version of WeinerNoiseReduction by Pascal Scalart (2009)
Y is power spectral density of noisy speech
N is power spectral density of noise-only portion of signal
H(f) is FFT of h(t). In this case h(t) ~= 1. For real system h(t) would have to do with acoustics of the car

## Slide 7: Background: Noise Gate
Parameters: Threshold, Attack, Release

## Slide 8: Evolutionary Strategy
(μ, λ) CMA-ES with weighted recombination
μ = 6,12,24 parents, λ = 12,24,48 offspring
Each offspring contains 8 parameters
Gw
Gs
Wiener(α)
SpecSub(N,H,L)
+
Gate(T,A/R)
Notes: Weighted recombination = best individuals are given higher weight when computing the new distribution mean

## Slide 9: Results
Three different run configurations
  1: Population of 12
  2: Population of 24
  3: Population of 48
300 Generations per run
50 runs per configuration

## Slide 10: Results
Notes: Shows average fitness at each generation number for each configuration type.
Only first 100 generations are shown since lines become steady after and to decrease clutter in graph
Population of 48 gets to better fitness a little faster
Population of 48 also arrives at a better overall fitness

## Slide 11: Results
Notes: Shows same average as previous slide, but with error bars showing the 95% confidence interval.
Overall error bars are pretty small
In all three cases, error bars get smaller as the number of generations increases.
  This is because the population is becoming less diverse.

## Slide 12: Results
 | Expert Results | Expert Results | Best Pop 12 | Best Pop 24 | Best Pop 48
% Wiener | 1 | 0 | 1.10 | 0.97 | 1.10
Alpha | 0.98 | - | 0.95 | 0.96 | 0.95
% Spectral | 0 | 1 | 0.41 | 0.45 | 0.41
Noise Length | - | 18 | 13.65 | 18.92 | 0.69
Noise Margin | - | 8 | 18.23 | 0.78 | 15.35
Hang Over | - | 3 | 9.33 | 0.58 | 18.16
Threshold | 0.03 | 0.03 | 0.03 | 0.03 | 0.03
Attack | 1.5 | 1.5 | 1.25 | 0.96 | 1.25
Fitness | 0.0301 | 0.0316 | 0.0225 | 0.0223 | 0.0225

## Slide 13: Results
Running the best results with only
the Wiener Filter
 | Expert Results | Best Results
% Wiener | 1 | 1
Alpha | 0.98 | 0.96
% Spectral | 0 | 0
Fitness | 0.0301 | 0.0240

## Slide 14: Results
Running the best results with only
Spectral Subtraction
 | Expert Results | Best Results
% Wiener | 0 | 0
% spectral | 1 | 1
%Noise Length | 18 | 18.92
Noise Margin | 8 | 0.78
Hang Over | 3 | 0.58
Fitness | 0.0316 | 0.0315

## Slide 15: Results
Clean File
Dirty File
Processed File

## Slide 16: Conclusions
We are able to improve upon the expert results with the use of Evolutionary Computation.
The larger the population the faster the best solution is found.
As the number of generations increases the population becomes less diverse.

## Slide 17
Questions?